## Slide 1: GUDA Introduction
林政宏
國立台灣師範大學電機系

## Slide 2: Nvidia Tesla P100
共包含60個SM（6GPC x 10SM）
SM(Streaming Multiprocessor):
  多個SP(Streaming Processor), 又稱 CUDA core
  其他硬體资源如：warp scheduler，register，shared memory等
  同一个block中的warp一定分配给同一個SM
  每個SM有自己獨立的local L1 cache，但所有SM會共用Device的L2 cache

## Slide 3: SM(Streaming Multiprocessor)
每個SM有自己的內部结構，如下圖所示GP100（Nvidia Tesla P100）中的SM內部结構，在GP100裡，每一個SM有左右兩個SM Processing Block（SMP）
SP(Streaming Processor):最基本的處理單元，也稱為CUDA core，表示在上圖中為綠色的小格子
  相當於一個簡易的CPU
  內部包括控制單元Dispatch Port、Operand Collector，以及浮點計算單元FP Unit、整數計算單元Int Unit，另外還包括計算結果隊列。當然還有Compare、Logic、Branch等

## Slide 4: SP(Streaming Processor)
最基本的處理單元，也稱為CUDA core，表示在上圖中為綠色的小格子
  相當於一個簡易的CPU
  內部包括控制單元Dispatch Port、Operand Collector，以及浮點計算單元FP Unit、整數計算單元Int Unit，另外還包括計算結果隊列。當然還有Compare、Logic、Branch等

## Slide 5: GPU Computing
GPU: Graphics Processing Unit
Traditionally used for real-time rendering
High computational density (100s of ALUs) and memory bandwidth (100+ GB/s)
Throughput processor: 1000s of concurrent threads to hide latency (vs. large fast caches)

## Slide 6: Software Concept in CUDA
Thread：一個CUDA的並行程序會被分配到多個threads來執行
  一個SP對應執行一個thread
  threadId在cuda中為三維的概念，在一個block中由(x, y, z)來唯一定位
Block：多個thread群組成一個block
  同一個block中的threads可以同步，也可以通過shared memory通信
  blockId在cuda中為二維的概念，在一個grid中由(x, y)來唯一定位
Grid：多個block構成grid
  一個grid對應一個執行一個kernel函數
warp：執行任務的調度單元，同一時間一個SM只能運行一個warp
  類比於CPU中的進程，當一個warp阻塞時，SM將切換執行另一個warp
  當前CUDA的warp大小為32個線程。同在一個warp中的線程，以不同數據資源執行相同的指令，即所謂的SIMT（Single Instruction Multiple Thread）

## Slide 7: CPU與GPU結構對比
The CPU relies on larger caches and complex logic control (such as pipeline, out-of-order execution, instruction prediction and preprocessing, etc.) to hide the delay
GPU relies on higher parallelism to hide the delay

## Slide 8: Floating-Point Operations per Second for the CPU and GPU

## Slide 9: Memory Bandwidth for the CPU and GPU

## Slide 10: CUDA ™: A General-Purpose Parallel Computing Platform and Programming Model
CUDA : Compute Unified Device Architecture
  CUDA is a compiler and toolkit for programming NVIDIA GPUs
  Enable heterogeneous computing and horsepower of GPUs
  CUDA API extends the C/C++ programming language
  Express SIMD parallelism
  Give a high level abstraction from hardware

## Slide 11: CUDA software stack
CUDA library
  Programming language function API
CUDA runtime API
  High-level API
CUDA driver API
  Low-level API

## Slide 12: CUDA Program Flow

## Slide 13: CUDA Program Flow

## Slide 14: CUDA Program Flow

## Slide 15: CUDA Programming Model
CUDA = serial program with parallel kernels, all in C
  Serial C code executes in a host thread (i.e. CPU thread)
  Parallel kernel C code executes in many devices threads across multiple processing elements (i.e. GPU threads)

## Slide 16: CUDA program framework
#include <cuda_runtime.h>
__global__ void my_kernel(…) { … }
int main() { … cudaMalloc(…) cudaMemcpy(…) … my_kernel<<<nblock,blocksize>>>(…) … cudaMemcpy(…) … }
GPU code (parallel)
CPU code
(serial or parallel if
p-thread/OpenMP/T
BB/MPI is used.)

## Slide 17: Kernel = Many Concurrent Threads
One kernel is executed at a time on the device
Many thread execute each kernel
  Each thread executes the same code
  … on the different data based on its threadID
CUDA thread might be
  Physical threads
    As on NVIDIA GPUs
    GPU thread creation and context switching are essentially free
  Or virtual threads
    E.g. 1 CPU core might execute multiple CUDA threads

## Slide 18: Thread Hierarchy
Threads are grouped into thread blocks
  Kernel = gird of thread blocks
By definition, threads in the same block may synchronized with barriers, but not between blocks

## Slide 19: Software Mapping
Software: grid  blocks  threads
Hardware: GPU(device)  SM(Streaming Multiprocessor)  SP(Streaming Processor), 又稱 CUDA core

## Slide 20: Scheduling Thread Blocks
Hardware dispatches thread blocks to available processor (streaming multiprocessor)

## Slide 21: Scheduling Thread Blocks
A GPU has lots of processors (streaming multiprocessors)
Each processor (streaming multiprocessors) can execute multiple blocks concurrently
  Programmers need to ensure that kernel launches creates enough thread blocks to keep machine busy
Hardware dispatches a block when resources become available, typically when a previous block completes
  No specific order in which blocks are dispatched and executed
  Design algorithms to be insensitive to block execution order

## Slide 22: Automatic Scalability
Thread blocks cannot synchronize
  So they can run in any order, concurrently or sequentially
This independence gives scalability:
  A kernel scales across any number of parallel cores

## Slide 23: Some Restrictions First
All threads in a grid execute the same kernel function
A grid is organized as a 3D array of blocks (gridDim.x and gridDim.y, gridDim.z)
Each block is organized as 3D array of threads (blockDim.x, blockDim.y, and blockDim.z)
Once a kernel is launched, its dimensions cannot change.
All blocks in a grid have the same dimension
Once assigned to the SM, the block must be fully executed by the SM.

## Slide 24: Thread group limits
The maximum number of threads per block is limited
  512 before CUDA 2.0
  1024 after CUDA 2.0
The maximum number of blocks is limited
  65535 before CUDA 3
  2 31 -1 after CUDA 3
Total number of threads = threads per block * number of blocks

## Slide 25: GPU parameters
Name: GeForce GTX TITAN X
Compute capability: 5.2
Clock rate: 1076000
Device copy overlap: Enabled
Kernel execution timeout : Enabled
--- Memory Information for device 0 ---
Total global mem: 12802785280
Total constant Mem: 65536
Max mem pitch: 2147483647
Texture Alignment: 512
--- MP Information for device 0 ---
Multiprocessor count: 24
Shared mem per mp: 49152
Registers per mp: 65536
Threads in warp: 32
Max threads per block: 1024
Max thread dimensions: (1024, 1024, 64)
Max grid dimensions: (2147483647, 65535, 65535)
Name: GeForce GTX 480
Compute capability: 2.0
Clock rate: 1401000
Device copy overlap: Enabled
Kernel execution timeout : Disabled
--- Memory Information for device 1 ---
Total global mem: 1545732096
Total constant Mem: 65536
Max mem pitch: 2147483647
Texture Alignment: 512
--- MP Information for device 1 ---
Multiprocessor count: 15
Shared mem per mp: 49152
Registers per mp: 32768
Threads in warp: 32
Max threads per block: 1024
Max thread dimensions: (1024, 1024, 64)
Max grid dimensions: (65535, 65535, 65535)

## Slide 26: Memory Hierarchy

## Slide 27: Heterogeneous Computing
Terminology:
Host: The CPU and its memory (host memory)
Device: The GPU and its memory (device memory)
Host
Device

## Slide 28: Heterogeneous Programming
Host : CPU
Device : GPU
Kernel : functions executed on GPU
Thread : the basic execution unit
Block : a group of threads
Grid : a group of blocks

## Slide 29: CUDA Language
Philosophy: provide minimal set of extensions necessary
Kernel launch
  kernelFunc<<< nB, nT, nS, Sid >>>(…); // nS and Sid are optional
    nB：number of blocks per grid (grid size)
    nT：number of threads per block (block size)
    nS：shared memory size (in bytes)
    Sid： stream ID, default is 0
Build-in device variables
  threadIdx; blockIdx; blockDim; gridDim
Intrinsic functions that expose operations in kernel code
  __syncthreads();
Declaration specifier to indicate where things live
  __global__ void KernelFunc(…); // kernel function, run on device
  __device__ void GlobalVar; // variable in device memory
  __shared__ void SharedVar; // variable in per-block shared memory

## Slide 30: Block IDs and Thread IDs
Each block and thread uses IDs to decide what data to work on
  dim3 blockIdx;
    blockIdx.x, blockIdx.y, blockIdx.z
  dim3 threadIdx;
    threadIdx.x, threadIdx.y, threadIdx.z
  dim3 gridDim;
    gridDim.x, gridDim.y, gridDim.z
  dim3 blockDim;
    blockDim.x, blockDim.y, blockDim.z

## Slide 31: Function Qualifiers
Function qualifiers | limitations
__device__ function | Executed on the device Callable from the device only
__global__ function | Executed on the device Callable from the host only (must have void return type!)
__host__ function | Executed on the host Callable from the host only
Functions without qualifiers | Compiled for the host only
__host__ __device__ function | Compiled for both the host and the device

## Slide 32: Variable Type Qualifiers
Variable qualifiers | limitations
__device__ var | Resides in device’s global memory space Has the lifetime of an application Is accessible from all the threads within the grid and from the host through the runtime library
__constant__ var | Resides in device’s constant memory space
__shared__ var | Resides in the shared memory space of a thread block Has the lifetime of the block Is only accessible from all the threads within the block

## Slide 33: CUDA Runtime API
Device management
  cudaGetDeviceCount(), cudaGetDeviceProperties()
Device memory management
  cudaMalloc(), cudaFree(), cudaMemcpy()
Graphic interoprability
  cudaGLMapBufferObject(), cudaD3DMapResources()
Texture management
  cudaBindTexture(), cudaBindTextureToArray()

## Slide 34: Device memory operations
Three functions:
cudaMalloc(), cudaFree(), cudaMemcpy()
Similar to the C’s malloc(), free(), memcpy()
cudaMalloc(void **devPtr, size_t size)
  devPtr : return the address of the allocated device memory
  size : the allocated memory size (bytes)
cudaFree (void *devPtr)
cudaMemcpy( void *dst, const void *src, size_t count, enum cudaMemcpyKind kind)
  count : size in bytes to copy

## Slide 35: cudaMemcpyKind
one of the following four values
cudaMemcpyKind | Meaning | dst | src
cudaMemcpyHostToHost | Host  Host | host | host
cudaMemcpyHostToDevice | Host  Device | Device | Host
cudaMemcpyDeviceToHost | Device  Host | Host | Device
cudaMemcpyDeviceToDevice | Device  Device | Device | Device
host to host has the same effect as memcpy()

## Slide 36: Program Compilation
Any source file containing CUDA language must be compiled with NVCC
  NVCC separates code running on the host from code running on the device
Two-stage complication:
  Virtual ISA
    PTX: Parallel Threads eXecutions
  Device-specific binary object

## Slide 37: Example 1: Hello World!
Two new syntactic elements…
  1. __global__ indicates a function that runs on the device and is called from host code
  2. mykernel<<<1,1>>>();
  Triple angle brackets mark a call from host code to device code, which is called a “kernel launch”.
__global__ void mykernel(void) {
}
int main(void) {
mykernel<<<1,1>>>();
printf("Hello World!\n");
return 0;
}

## Slide 38: Example 2: add 2 numbers
This does not work!!
int ha, hb, hc are in the host memory (DRAM), which cannot be used by device (GPU).
We need to allocate variables in “device memory”.
__global__ void add(int *a, int *b, int *c) {
*c = *a + *b;
}
int main(void) {
int ha=1,hb=2,hc;
add<<<1,1>>>(&ha, &hb, &hc);
printf(“c=%d\n”,hc);
return 0;
}
x

## Slide 39: The correct main()
int main(void) {
int a=1, b=2, c; // host copies of a, b, c
int *d_a, *d_b, *d_c; // device copies of a, b, c
// Allocate space for device copies of a, b, c
cudaMalloc((void **)&d_a, sizeof(int));
cudaMalloc((void **)&d_b, sizeof(int));
cudaMalloc((void **)&d_c, sizeof(int));
// Copy inputs to device
cudaMemcpy(d_a,&a,sizeof(int),cudaMemcpyHostToDevice);
cudaMemcpy(d_b,&b,sizeof(int),cudaMemcpyHostToDevice);
// Launch add() kernel on GPU
add<<<1,1>>>(d_a, d_b, d_c);
// Copy result back to host
cudaMemcpy(&c, d_c, size, cudaMemcpyDeviceToHost);
// Cleanup
cudaFree(d_a); cudaFree(d_b); cudaFree(d_c);
return 0;
}


## Slide 40: Example 3: add 2 vectors
Let’s first look at the sequential code!
// function definition
void VecAdd(int N, float* A, float* B, float* C)
{
for(int i = 0; i<N; i++)
C[i] = A[i] + B[i];
}
int main()
{ ...
VecAdd (N, Ah, Bh, Ch);
...
}

## Slide 41: Parallel CUDA code
Use threadIdx.x as the index of the arrays
Each thread processes 1 addition, for the elements indexed at threadIdx.x .
// Kernel definition
__global__ void VecAdd(float* A, float* B, float* C)
{
int i = threadIdx.x;
C[i] = A[i] + B[i];
}
int main()
{ ...
// Kernel invocation with N threads
VecAdd<<<1, N>>>(Ah, Bh, Ch); ...
}
What is the limit of N?

## Slide 42: N=4 case
Four threads can be executed in parallel.
Each thread has a unique threadIdx , starting from 0.
threadIdx is a build-in variable, which is a structure of 3 members: x , y , and z .
  struct unit3 { x; y; z; };
  struct dim3 { x; y; z; };
c[0] = a[0] + b[0]
Thread 0
c[1] = a[1] + b[1]
Thread 1
c[2] = a[2] + b[2]
Thread 2
c[3] = a[3] + b[3]
Thread 3

## Slide 43: Alternative implementation
Using parallel thread instead
N blocks and each block has 1 thread.
Which one is better?
  Threads in the same block can communicate, synchronize with others, but the number of threads per block is limited.
__global__ void add(int *a, int *b, int *c) {
c[blockIdx.x] = a[blockIdx.x] + b[blockIdx.x];
}
int main(void) {
int a[N], b[N], c[N];
int *d_a, *d_b, *d_c;
...
add<<< N, 1 >>>(d_a, d_b, d_c);
...
}

## Slide 44: 3rd implementation
Using multiple threads and multiple blocks
Suppose N=16, grid size = 4, and block size = 4
How to index 16 elements of an array?
  Method 1: index = blockIdx.x*4+threadIdx.x
  Method 2: index = threadIdx.x*4+blockIdx.x
Which one is better?
blockIdx.x = 0
threadIdx.x=
0
1
2
3
blockIdx.x = 1
threadIdx.x=
0
1
2
3
blockIdx.x = 2
threadIdx.x=
0
1
2
3
blockIdx.x = 3
threadIdx.x=
0
1
2
3
0
1
2
3
12
13
14
15
4
5
6
7
8
9
10
11

## Slide 45: 3rd implementation
Using multiple threads and multiple blocks
Suppose N=16, grid size = 4, and block size = 4
How to index 16 elements of an array?
  Method 1: index = blockIdx.x*4+threadIdx.x
  Method 2: index = threadIdx.x*4+blockIdx.x
Which one is better?
blockIdx.x = 0
threadIdx.x=
0
1
2
3
blockIdx.x = 1
threadIdx.x=
0
1
2
3
blockIdx.x = 2
threadIdx.x=
0
1
2
3
blockIdx.x = 3
threadIdx.x=
0
1
2
3
0
1
2
3
12
13
14
15
4
5
6
7
8
9
10
11
memory coalesced

## Slide 46: The general case
Use the built-in variable blockDim.x for threads per block.
BS is block size (number of threads per block)
__global__ void add(int *a, int *b, int *c) {
int index = threadIdx.x + blockIdx.x * blockDim.x;
c[index] = a[index] + b[index];
}
int main(void) {
int a[N], b[N], c[N];
int *d_a, *d_b, *d_c;
...
add<<< N/BS,BS>>>(d_a, d_b, d_c);
...
}
What if N is not a
multiple of BS ?

## Slide 47: A even more general case
The kernel function can have branches, but with a price to pay…
__global__ void add(int *a, int *b, int *c, int n) {
int index = threadIdx.x + blockIdx.x * blockDim.x;
if (index < n)
c[index] = a[index] + b[index];
}
int main(void) {
int a[N], b[N], c[N];
int *d_a, *d_b, *d_c;
...
add<<< (N+BS-1)/BS, BS>>>(d_a, d_b, d_c, N);
...
}

## Slide 48: Execution time: in host
CUDA provides functions to measure the execution time between events.
cudaError_t cudaEventElapsedTime( float* ms, cudaEvent_t start, cudaEvent_t end)
  ms: time between start and end in ms
  start: starting event
  end: ending event
The time unit is milliseconds, whose resolution is 0.5 microseconds

## Slide 49: CUDA event
Data type：cudaEvent_t
cudaError_t cudaEventCreate(cudaEvent_t* event)
  Create CUDA event
cudaError_t cudaEventRecord(cudaEvent_t event, cudaStream_t stream = 0)
  Record CUDA event
  If stream is non-zero, the event is recorded after all preceding operations in the stream have been completed
  Since operation is asynchronous, cudaEventQuery() and/or cudaEventSynchronize() must be used to determine when the event has actually been recorded
cudaError_t cudaEventSynchronize(cudaEvent_t event)
  Wait until the completion of all device work preceding the most recent call to cudaEventRecord()

## Slide 50: Example
1. cudaEvent_t start, stop;
2. cudaEventCreate(&start);
3. cudaEventCreate(&stop);
4. cudaEventRecord(start);
5. kernel<<<block, thread>>>();
6. cudaEventRecord(stop);
7. cudaEventSynchronize(stop);
8. float time;
9. cudaEventElapsedTime(&time, start, stop);

## Slide 51: Device information
Query device information by
cudaGetDeviceProperties(struct cudaDeviceProp *prop, int device)
  cudaDeviceProp is a structure, which specifies properties for the queried device
    char name[256];
    int maxThreadsPerBlock;
    int maxThreadsDim[3];
    int maxGridSize[3];
    int clockRate;
    ...
  Device is the device number, specifying which device’s information is queried (used in multi-GPU environment)

## Slide 52: Host and device sync
Kernel launches are asynchronous
  Control returns to the CPU immediately
  CPU needs to synchronize before consuming the results.
  cudaDeviceSynchronize() blocks the CPU until all preceding CUDA calls have completed
cudaMemcpy() blocks the CPU until the copy is complete
  Copy begins when all preceding CUDA calls have completed
  Using cudaMemcpyAsync() to perform asynchronous memory copy, which does not block the CPU

## Slide 53: Reporting errors
All CUDA calls return an error code cudaError_t
  Error in the API call itself OR Error in an earlier asynchronous operation (e.g. kernel)
Get the error code for the last error:
  cudaError_t cudaGetLastError(void)
Get a string to describe the error:
  char *cudaGetErrorString(cudaError_t)

## Slide 54: Device Management
Application can query and select GPUs
  cudaGetDeviceCount(int *count)
  cudaSetDevice(int device)
  cudaGetDevice(int *device)
  cudaGetDeviceProperties(cudaDeviceProp *prop, int device)
Multiple CPU threads can share a device
A single CPU thread can manage multiple devices
  cudaSetDevice(i) to select current device
  cudaMemcpy(…) for peer-to-peer copies

## Slide 55: Occupancy
Occupancy: number of concurrent threads per SM
  Expressed as either:
    the number of threads (or warps)
    percentage of maximum threads
Determined by several factors
  (refer to Occupancy Calculator, CUDA Programming Guide for full details)
  Registers per thread
    SM registers are partitioned among the threads
  Shared memory per block
    SM shared memory is partitioned among the blocks
  Threads per block
    Threads are allocated at threadblock granularity

## Slide 56: Occupancy and Performance
Note that 100% occupancy isn’t needed to reach maximum performance
  Sufficient occupancy to hide latency, higher occupancy will not improve performance
“Sufficient” occupancy depends on the code
  More independent work per thread → less occupancy is needed
  Memory-bound codes tend to need higher occupancy
    Higher latency (than for arithmetic) needs more work

## Slide 57: CUDA LAB 1: Vector Addition

## Slide 58: Vector Addition

## Slide 59: CPU Version

## Slide 60: Dual Core Version

## Slide 61: CUDA Built-in Variables
dim3 gridDim;
  Dimensions of the grid in blocks
  gridDim.x, gridDim.y, gridDim.z
dim3 blockDim;
  Dimensions of the block in threads
  blockDim.x, blockDim.y, blockDim.z
dim3 blockIdx;
  Block index within the grid
  blockIdx.x, blockIdx.y, blockIdx.z
dim3 threadIdx;
  Thread index within the block
  threadIdx.x, threadIdx.y, threadIdx.z

## Slide 62: First GPU vector addition

## Slide 65: Multiple Blocks Single Thread
add<<<N,1>>>( dev_a, dev_b, dev_c );
N blocks x 1 thread/block = N parallel threads
……
c[0] = a[0] + b[0];
Block 0
c[1] = a[1] + b[1];
c[2] = a[2] + b[2];
c[3] = a[3] + b[3];
Block 1
Block 2
Block 3

## Slide 66: Problem
N is changed to 1024x1024
Increase the number of blocks
What is the limitation of blocks???
Each block must handle more than one position.
……
……
……
……
……

## Slide 67: ANS
add<<<N, 1>>>( dev_a, dev_b, dev_c );
N blocks x 1 thread/block = N parallel threads
……
__global__ void add( int *a, int *b, int *c ) {
int tid = blockIdx.x;
while (tid < N)
c[tid] = a[tid] + b[tid];
tid += gridDim.x;
}

## Slide 68: Single Block Multiple Threads
Terminology: a block can be split into parallel threads
add<<<1, N>>>( dev _ a, dev _ b, dev _ c );
__global__ void add( int *a, int *b, int *c ) {
int tid = threadIdx.x;
if (tid < N)
c[tid] = a[tid] + b[tid];
}
……
c[0] = a[0] + b[0];
Thread 0
c[1] = a[1] + b[1];
c[2] = a[2] + b[2];
c[3] = a[3] + b[3];
Thread 1
Thread 2
Thread 3

## Slide 69: Problem
N is changed to 1024x1024
Increase the number of threads per block???
What is the limitation of threads per blocks???
Each thread must handle more than one position.
……
……
……
……
……

## Slide 70: ANS
add<<<1, N>>>( dev _ a, dev _ b, dev _ c );
__global__ void add( int *a, int *b, int *c ) {
int tid = threadIdx.x;
while (tid < N)
c[tid] = a[tid] + b[tid];
tid += blockDim.x;
}
……

## Slide 71: Combining Blocks and Threads
We’ve seen parallel vector addition using:
  Many blocks with one thread each
  One block with many threads
Let’s adapt vector addition to use both blocks and threads

## Slide 72: Indexing Arrays with Blocks and Threads
No longer as simple as using blockIdx.x and threadIdx.x
  Consider indexing an array with one element per thread (8 threads/block)
With M threads/block a unique index for each thread is given by:
  int index = threadIdx.x + blockIdx.x * M (blockDim.x);

## Slide 73: Multiple Blocks Multiple Threads
add<<< 1024/32, 32>>>( dev _ a, dev _ b, dev _ c );
int tid = threadIdx.x + blockIdx.x * blockDim.x;
__global__ void add( int *a, int *b, int *c ) {
int tid = threadIdx.x + blockIdx.x * blockDim.x;
if (tid < N) {
c[tid] = a[tid] + b[tid];
}
}
……
……
……
……

## Slide 74: Problem
N is changed to 1024x1024
Increase the number of blocks
What is the limitation of blocks???
Each thread must handle more than one position.
……
……
……
……
……
……
……
……
……
……
……
……

## Slide 75: ANS
unsigned int threadsPerBlock = 32; //最大為1024
unsigned int blocksPerGrid = (N + threadsPerBlock - 1)/threadsPerBlock;
add <<< blocksPerGrid, threadsPerBlock >>> ( dev_a, dev_b, dev_c );
__global__ void add( int *a, int *b, int *c ) {
int tid = threadIdx.x + blockIdx.x * blockDim.x;
while (tid < N) {
c[tid] = a[tid] + b[tid];
tid += blockDim.x * gridDim.x;
}
}
……
……
……
……

## Slide 76: Note
blocksPerGrid cannot exceed the maximum gridDim.x
因此total最大的thread數量將會是2147483647 x 1024
如果N大於2147483647 x 1024 ???

## Slide 77: Time counting on Linux
struct timespec t_start, t_end; double elapsedTime; // start time clock_gettime( CLOCK_REALTIME, &t_start); // do something // stop time clock_gettime( CLOCK_REALTIME, &t_end); // compute and print the elapsed time in millisec elapsedTime = (t_end.tv_sec - t_start.tv_sec) * 1000.0; elapsedTime += (t_end.tv_nsec - t_start.tv_nsec) / 1000000.0; printf("elapsedTime: %lf ms\n", elapsedTime);
Linux:// compile with -lrt #include <time.h>

## Slide 78: GPU time counting
// Get start time event
cudaEvent_t start, stop;
cudaEventCreate(&start);
cudaEventCreate(&stop);
cudaEventRecord(start, 0);
// Invoke kernel here
// Get stop time event
cudaEventRecord(stop, 0);
cudaEventSynchronize(stop);
// Compute execution time
float elapsedTime;
cudaEventElapsedTime(&elapsedTime, start, stop);
printf("GPU time: %13f msec\n", elapsedTime);
cudaEventDestroy(start);
cudaEventDestroy(stop);

## Slide 79: CUDA LAB 2: Vector Dot Product

## Slide 80: Dot Product

## Slide 81
const int N = 1024;
const int threadsPerBlock = 1024;
const int blocksPerGrid = 1;
__global__ void dot( int *a, int *b, int *c ) {
int tid = threadIdx.x;
if (tid < N) {
c[tid] = a[tid] * b[tid];
}
__syncthreads();
int i = N / 2;
while (i != 0) {
if (tid < i){
c[tid] += c[tid + i];
}
__syncthreads();
i /= 2;
}
}

## Slide 82: Single Block Multiple Thread
……

## Slide 83: Problem
N is changed to 1024x1024
Each thread must handle more than one position.
……

## Slide 84: ANS

## Slide 85: Thinking
May we modify the above code using multiple block multiple thread?
……
……
……
……

## Slide 86
const int N = 1024 *1024;
const int threadsPerBlock = 1024;
const int blocksPerGrid = N / 1024;
__global__ void dot( int *a, int *b, int *c ) {
__shared__ int cache[threadsPerBlock];
int tid = threadIdx.x + blockIdx.x * blockDim.x;
int cacheIndex = threadIdx.x;
cache[cacheIndex] = a[tid] * b[tid];
__syncthreads();
int i = blockDim.x/2;
while (i != 0) {
if (cacheIndex < i)
cache[cacheIndex] += cache[cacheIndex + i];
__syncthreads();
i /= 2;
}
if (cacheIndex == 0)
c[blockIdx.x] = cache[0];
}

## Slide 87: Thinking
If N = 64 *1024 *1024
const int blocksPerGrid = N / 1024;
blocksPerGrid will exceed 65535 (the maximum blocks for GTX480)
How to modify the example code?

## Slide 88
const int N = 64 * 1024 * 1024;
const int threadsPerBlock = 1024;
const int blocksPerGrid = 1024;
__global__ void dot( int *a, int *b, int *c ) {
__shared__ int cache[threadsPerBlock];
int tid = threadIdx.x + blockIdx.x * blockDim.x;
int cacheIndex = threadIdx.x;
int temp = 0;
while (tid < N) {
temp += a[tid] * b[tid];
tid += blockDim.x * gridDim.x;
}
// set the cache values
cache[cacheIndex] = temp;
__syncthreads();

## Slide 89: Optimized version using shared memory

## Slide 90: CUDA LAB 3: Matrix Multiplication

## Slide 91: Square Matrix Multiplication
P = M * N of size WIDTH x WIDTH
One thread calculates one element of P
M and N are loaded WIDTH times from global memory
M
N
P
WIDTH
WIDTH
WIDTH
WIDTH

## Slide 92: Memory Layout of a Matrix in C
M2,0
M1,1
M1,0
M0,0
M0,1
M3,0
M2,1
M3,1
M1,2
M0,2
M2,2
M3,2
M1,3
M0,3
M2,3
M3,3
M2,0
M1,0
M0,0
M3,0
M1,1
M0,1
M2,1
M3,1
M1,2
M0,2
M2,2
M3,2
M1,3
M0,3
M2,3
M3,3
M

## Slide 93: A Single Thread Version in C
__global__ void MatMulKernel(float *Md, float *Nd, float *Pd, int width)
{
for(int i = 0; i < width; ++i){
for(int j = 0; j < width; ++j){
// Computes one element of P
float Pvalue = 0;
for(int k = 0; k < width; ++k){
float Melement = *(Md + i*width + k);
float Nelement = *(Nd + k*width + j);
Pvalue += Melement * Nelement;
}
*(Pd + i*width + j) = Pvalue;
}
}
}
M
N
P
WIDTH
WIDTH
WIDTH
WIDTH
i
k
k
j

## Slide 94: Input Matrix Data Transfer
void MatMul(float *M, float *N, float *P, int width)
{
size_t size = width * width * sizeof(float);
float *Md, *Nd, *Pd;
// Allocate and Load M, N to device memory
cudaMalloc((void **)&Md, size);
cudaMemcpy(Md, M, size, cudaMemcpyHostToDevice);
cudaMalloc((void **)&Nd, size);
cudaMemcpy(Nd, N, size, cudaMemcpyHostToDevice);
// Allocate P on the device
cudaMalloc((void **)&Pd, size);

## Slide 95: Output Matrix Data Transfer
// Invoke kernel & record time – to be shown later
......
// Read P from device memory
cudaMemcpy(P, Pd, size, cudaMemcpyDeviceToHost);
// Free device memory
cudaFree(Md);
cudaFree(Nd);
cudaFree(Pd);
}

## Slide 96: Setting and Invoke kernel
// Setup the execution configuration
dim3 dimGrid(1, 1);
dim3 dimBlock(width, width);
// Get start time event
cudaEvent_t start, stop;
cudaEventCreate(&start);
cudaEventCreate(&stop);
cudaEventRecord(start, 0);
// Invoke kernel
// Get stop time event
cudaEventRecord(stop, 0);
cudaEventSynchronize(stop);
MatMulKernel<<<dimGrid, dimBlock>>>(Md, Nd, Pd, width);

## Slide 97: Timing
// Setup the execution configuration
dim3 dimGrid(1, 1);
dim3 dimBlock(width, width);
// Get start time event
cudaEvent_t start, stop;
cudaEventCreate(&start);
cudaEventCreate(&stop);
cudaEventRecord(start, 0);
// Invoke kernel
// Get stop time event
cudaEventRecord(stop, 0);
cudaEventSynchronize(stop);
MatMulKernel<<<dimGrid, dimBlock>>>(Md, Nd, Pd, width);
// Compute execution time
float elapsedTime;
cudaEventElapsedTime(&elapsedTime,start,stop);
printf("GPU time: %13f msec\n", elapsedTime);
cudaEventDestroy(start);
cudaEventDestroy(stop);

## Slide 98: Kernel Function
void MatMulKernel(float *Md, float *Nd, float *Pd, int width)
{
int row = threadIdx.y;
int col = threadIdx.x;
float Pvalue = 0;
for (int k = 0; k < width; ++k) {
float Melement = *(Md + row*width + k);
float Nelement = *(Nd + k*width + col);
Pvalue += Melement * Nelement;
}
*(Pd + row*width + col) = Pvalue;
}
M
N
P
WIDTH
WIDTH
WIDTH
WIDTH
row
k
k
col

## Slide 99: Only One Thread Block Used
One Block of threads compute matrix Pd
  Each thread computes one element of Pd
Each thread
  Loads a row of matrix Md
  Loads a column of matrix Nd
  Perform one multiply and addition for each pair of Md and Nd elements
  Compute to off-chip memory access ratio close to 1:1 (not very high)‏
Size of matrix limited by the number of threads allowed in a thread block
Grid 1
Block 1
48
Thread
(2, 2)‏
WIDTH
Md
Pd
Nd

## Slide 100: Matrix Multiplication Using Multiple Blocks
Break-up Pd into tiles
Each block calculates one tile
  Each thread calculates one element in a tile
  Block size equal tile size
Md
Nd
Pd
Pdsub
TILE_WIDTH
WIDTH
WIDTH
bx
tx
0
1
TILE_WIDTH-1
2
0
1
2
by
ty
2
1
0
TILE_WIDTH-1
2
1
0
TILE_WIDTHE
WIDTH
WIDTH

## Slide 101: A Small Example
P1,0
P0,0
P0,1
P2,0
P3,0
P1,1
P0,2
P2,2
P3,2
P1,2
P3,1
P2,1
P0,3
P2,3
P3,3
P1,3
Block(0,0)
Block(1,0)
Block(1,1)
Block(0,1)
TILE_WIDTH = 2
Pd1,0
Md2,0
Md1,1
Md1,0
Md0,0
Md0,1
Md3,0
Md2,1
Pd0,0
Md3,1
Pd0,1
Pd2,0
Pd3,0
Nd0,3
Nd1,3
Nd1,2
Nd1,1
Nd1,0
Nd0,0
Nd0,1
Nd0,2
Pd1,1
Pd0,2
Pd2,2
Pd3,2
Pd1,2
Pd3,1
Pd2,1
Pd0,3
Pd2,3
Pd3,3
Pd1,3

## Slide 102
// Setup the execution configuration
dim3 dimBlock(16, 16);
dim3 dimGrid(width/16, width/16);
// Invoke kernel
MatMulKernel<<<dimGrid, dimBlock>>>(Md, Nd, Pd, width);
__global__ void MatMulKernel(float *Md, float *Nd, float *Pd, int width)
{
// Thread row and column within matrix
int row = blockIdx.y * blockDim.y + threadIdx.y;
int col = blockIdx.x * blockDim.x + threadIdx.x;

## Slide 103
// Matrix multiplication kernel called by MatMul()
__global__ void MatMulKernel(float *Md, float *Nd, float *Pd, int width)
{
// Thread row and column within matrix
int row = blockIdx.y * blockDim.y + threadIdx.y;
int col = blockIdx.x * blockDim.x + threadIdx.x;
// Each thread computes one element of P
// by accumulating results into Pvalue
float Pvalue = 0;
// Multiply M and N
for (int k = 0; k < width; ++k) {
float Melement = *(Md + row*width + k);
float Nelement = *(Nd + k*width + col);
Pvalue += Melement * Nelement;
}
// Write Pvalue to device memory
// Each thread writes one element
*(Pd + row*width + col) = Pvalue;
}

## Slide 104: Tiled Multiply
Break up the execution of the kernel into phases so that the data accesses in each phase is focused on one subset (tile) of Md and Nd
Each block computes one square sub-matrix Pdsub of size TILE_WIDTH
Each thread computes one element of Pdsub
Md
Nd
Pd
Pdsub
TILE_WIDTH
WIDTH
WIDTH
TILE_WIDTH
TILE_WIDTH
bx
tx
0
1
TILE_WIDTH-1
2
0
1
2
TILE_WIDTH
TILE_WIDTH
TILE_WIDTHE
WIDTH
WIDTH
by
ty
2
1
0
TILE_WIDTH-1
2
1
0
m
bx
k
by
m
k

## Slide 105
// Matrix multiplication kernel called by MatMul()
__global__ void MatMulKernel(float *Md, float *Nd, float *Pd, int width)
{
// Block row and column
int blockRow = blockIdx.y;
int blockCol = blockIdx.x;
// Each block computes one sub-matrix Psub of P
float *Pd_sub = GetSubMatrix(Pd, blockRow, blockCol, width);
// Thread row and column within sub-matrix
int row = threadIdx.y;
int col = threadIdx.x;
// Each thread computes one element of Psub
// by accumulating results into Pvalue
float Pvalue = 0;

## Slide 106
// Loop over all the sub-matrices of M and N that are
// required to compute Psub
for (int m = 0; m < (width / TILE_WIDTH); ++m) {
// Get sub-matrix Msub of M and N
float *Md_sub = GetSubMatrix(Md, blockRow, m, width);
float *Nd_sub = GetSubMatrix(Nd, m, blockCol, width);
// Multiply Msub and Nsub together
for (int k = 0; k < TILE_WIDTH; ++k) {
float Melement = GetElement(Md_sub, row, k, width);
float Nelement = GetElement(Nd_sub, k, col, width);
Pvalue += Melement * Nelement;
}
//Synchronize
__syncthreads();
}
// Write Psub to device memory
// Each thread writes one element
SetElement(Pd_sub, row, col, width, Pvalue);
}

## Slide 107: Performance Comparison
Multiple Block Multiplication
  Each thread: WIDTH*2 load from global memory (2 for M and N memory access)
  Each thread: WIDTH*2 mul/add operation (2 for mul and add)
  load:operation=1:1
Tiled Algorithm with shared memory
  Each tile: TILE_WIDTH2*2 load from global memory
  Each tile: TILE_WIDTH2*2*TILE_WIDTH mul/add operation
  Because each tile has TILE_WIDTH2 threads →
  Each thread: 2 load from global memory
  Each thread: 2*TILE_WIDTH mul/add operation
  load:operation=1:TILE_WIDTH
Notes: Tile width with shard memory的最大差異在load data from global memory to shared memory

## Slide 108: Invoke Tiled CUDA Kernel
size_t size = width * width * sizeof(float);
size_t shared_size = TILE_WIDTH * TILE_WIDTH * sizeof(float) * 2;
float *Md, *Nd, *Pd;
// Setup the execution configuration
dim3 dimGrid(width/TILE_WIDTH, width/TILE_WIDTH);
dim3 dimBlock(TILE_WIDTH, TILE_WIDTH);
// Invoke kernel
MatMulKernel<<<dimGrid, dimBlock, shared_size>>>(Md, Nd, Pd, width);

## Slide 109: Functions May be Used
// Get a matrix element
__device__ float GetElement(float *matrix, int row, int col, int width)
{
return *(matrix + row*width + col);
}
// Set a matrix element
__device__ void SetElement(float *matrix, int row, int col, int width, float value)
{
*(matrix + row*width + col) = value;
}
// Get the TILE_WIDTHxTILE_WIDTH sub-matrix matsub of matrix that is
// located col sub-matrices to the right and row sub-matrices down
// from the upper-left corner of matrix
__device__ float *GetSubMatrix(float *matrix, int blockrow, int col, int blockwidth)
{
return (matrix + blockrow*TILE_WIDTH*width + blockcol*TILE_WIDTH);
}

## Slide 110: Tiled Matrix Multiplication Kernel
__global__ void MatMulKernel(float *Md, float *Nd, float *Pd, int width) {
int blockRow = blockIdx.y; int blockCol = blockIdx.x;
float *Pd_sub = GetSubMatrix(Pd, blockRow, blockCol, width);
int row = threadIdx.y; int col = threadIdx.x;
float Pvalue = 0;
__shared__ float Mds[TILE_WIDTH][TILE_WIDTH];
__shared__ float Nds[TILE_WIDTH][TILE_WIDTH];
for (int m = 0; m < (width / TILE_WIDTH); ++m) {
float *Md_sub = GetSubMatrix(Md, blockRow, m, width);
float *Nd_sub = GetSubMatrix(Nd, m, blockCol, width);
Mds[row][col] = GetElement(Md_sub, row, col, width); // put Md_sub into shared memory
Nds[row][col] = GetElement(Nd_sub, row, col, width); // put Nd_sub into shared memory
__syncthreads();
for (int k = 0; k < TILE_WIDTH; ++k)
Pvalue += Mds[row][k] * Nds[k][col];
__syncthreads();
}
SetElement(Pd_sub, row, col, width, Pvalue);
}

## Slide 111: Parallel Prefix Sum
The all-prefix-sums operation takes a binary associative operator ⊕, and an array of n elements [a0 , a1 , …, an-1 ], and returns the array
[a0 , (a0 ⊕ a1 ), …, (a0 ⊕ a1 ⊕ … ⊕ an-1 )].
For example, given an array [3 1 7 0 4 1 6 3],
prefix sum would return [3 4 11 11 14 16 22 25].

## Slide 112: Sequential Scan
void scan( float* output, float* input, int length)
{
output[0] = 0; // since this is a prescan, not a scan
for(int j = 1; j < length; ++j)
{
output[j] = input[j-1] + output[j-1];
}
}

## Slide 113: Naïve Scan Algorithm

## Slide 115: Thrust - Introduction
Containers
  thrust::host_vector
  thrust::device_vector
Algorithms
  thrust::sort()
  thrust::reduce()
  thrust::inclusive_scan()